Handling:

- Ensure no children play near hay balers, carriers and stackers.

- Properly train operators handling tractors, front-end loaders or forklifts.

- Tractors with cabs, FOPS (falling object protective structure) or four-poster ROPS (roll-over protective structure) are highly recommended. Two-poster tractor ROPS offer no operator protection from bales falling back off of forks or bale-loading frames.

- Ensure bale-loading attachments on tractors and forklifts are secure and well fitted.

- Carry bales as low to the ground as possible.

- Ensure sufficient counterbalance on tractor or forklift vehicle.

- Hydraulic control valve should be specific to the front-end loader attachment.

Baler operation:

- Ensure baler is properly connected to the tractor.

- Make certain adequate safety guards are fitted.

- Nobody should ever be allowed to ride on the baler.

- Prevent others from getting too close to the baler.

- Watch for and clear any build-up of loose, combustible material in the baler.

- Ensure an updated fire extinguisher is fitted to the machine.

- Stop engine, disengage PTO and apply fly wheel brake (on square balers) prior to making adjustments or repairs.

- Extra care and attention should be made when reversing or turning the machine.

- Work during the day when there is adequate lighting.

Stacking:

- Land stack on even ground.

- Stacks should be clear of overhead powerlines.

- Stacked round bales should be adequately chocked and the borders posted.

- Watch for damaged bales at base of stack.

- Stack bales tightly and at a stable height.

- Do not stack bales higher than safe operating height of farm tractor or forklift.

- Do not allow children to play on stacked bales, particularly during stacking or unstacking.

- Do not handle more bales than is safe for the loader.

Transporting:

- Carry heavy loads of bales with a sturdy trailer.

- Ensure proper restraining frames on the back and front of trailer.

- Use fitted hooks so ropes can be used to secure load.

- Watch for overhead powerlines on or near roads.

- Avoid rough terrain that can cause bales to become unstable. Travel at safe speeds at all times.

- People should never ride on loaded hay trailers. This is highly dangerous.

Safety tips when working with bales and baling equipment:

- Keep children away from hay baling and stacking operations.

- Make sure operators and handlers are properly trained and physically capable of tasks.

- Consider fall-arrest protection for people working at heights.

- Use tractors with four-poster ROPS, FOPS or cabs for protection against falling bales.

- Replace risky attachments with manufacturer approved attachments.

- Ensure loader or forklift operators transport bales close to the ground.

- Avoid sharp turns and unsafe speeds.

- Make sure vehicle controls are fitted specifically for the attachment in use.

- Stacks should be on firm, level ground, away from fire hazards, sources of ignition, overhead powerlines, dwellings, property line fences and footpaths.

- Make sure stack and load heights do not exceed the lifting capabilities of the farm handling equipment.

- Stack big rectangular, square or high-density bales by overlapping to form a stable stack.

- Do not use bale lifting equipment to raise people on or off stacks.

- When transporting bales, be aware of overhead obstructions like trees, bridges and powerlines.

- Avoid rough ground that could cause bales to dislodge during transport.

- Ensure loads being transported are adequately secured. Do not overload vehicles beyond legal limits.

- Fire suppression capability must always be available during the baling operation.