| Company Information |
| --- |
| Company: | Workplace Location: |
| Prepared by: | Date: |
| TASK | HAZARD | LEVEL OF RISK | CONTROL METHOD |
| Opening up the grow room | Contact with steam | Low | Ensure room has steam turned off and is cooled. |
|  | Low oxygen | Low | Ensure room has been tested, signed off an unlocked by the Grower before entering. Door should have signage turned around and door lock removed |
| Setting up conveyor with skid steer | Oversize machinery Blind spots Run over/hit person/ equipment slipping | Moderate | Watch your feet, do not stand close the machine when the bobcat is moving it. Wear hi viz apparel. Steel toe boots. |
| Attach netting to pulling roller | Slipping Pinch points | Low | Do not put your hands on the net while rolling the net on the spool. |
| Line up truck under conveyor | Blind spots Run over/hit person/ equipment | Low | Trained Truck operator. Ensure path is clear. Ensure pre-trip inspection has been completed. |
| Unload the bed | Electric shock | Low | Steel toe boots. Ensure no cable on the ground. Ensure plug and hands are dry. Ensure plug and cables are in good condition. |
| Moving table down to next bed | Electric shock | Low | Ensure plug and hands are dry. Ensure plug and cables are in good condition. |
| Washing beds and floors | Slipping | Low | Steel toe boots. |
| Worker standing on ladder | Fall | Low | Ensure the rail guard is secured on the ladder platform before bringing the platform up. Ensure ladder inspection has been completed and ladder is in good condition. |
| Washing netting | Slipping Pinch points | Low | Steel toe boots. Do not put the hand on the spool while the net washer is operational. |
| Other Recommendations: Utilize frequent tailgate meetings to ensure all workers/contractors are aware of hazards. Other Safety Requirements (in addition to shaded requirements in header) Ensure Daily checklist is completed. Ensure all the Emergency stops are working. Ensure all the guards are in place. Ensure all the cables and remotes are in good condition. Keep work area neat at all times. DO NOT leave shovels, pitch forks, brooms, etc., lying on the floor. These are puncture and tripping hazards. Doors are to be FULLY opened before driving equipment in or out, then FULLY closed afterwards. This will enable you to avoid hitting doorways with oversize loads. DO NOT plug into electrical receptacles if they are wet or if the plug ends are wet. Report this to your Supervisor. Make sure 600V plugs are pushed together all the way and locked. This locks the plug in place. Turn Main switches off before unplugging or plugging-in machinery. When the 600-volt cords are “live” when you plug them in, “arcing” occurs inside the plug. When this is done enough times it becomes impossible to plug the cords in. |

# Text boxes

Disclaimer: This resource is intended for guidance and employers are advised to customize this document or design their own to meet their business needs and legal obligations. Once customized from its original content this disclaimer may be removed to function as part of your Safety Program. This resource does not relieve persons using it from their responsibilities under applicable legislation. If you need assistance contact us at www.AgSafeBC.ca