| Company Information |
| --- |
| Company: | Workplace Location: |
| Prepared by: | Date: |
| TASK | HAZARD | LEVEL OF RISK | CONTROL METHOD |
| Receiving straw | Slipping tripping and falling Collision with equipment or workers Dust exposure Impact from falling bales | Low | Wear steel toed boots with adequate grip Make sure that the straps holding the bales onto the truck have been safely removed and stored, Beware of trucks, equipment, and workers Ensure trucks have clear safe path to enter and exit ensure truck driver is at a safe distance from the unloading activity Workers to wear hi viz vests Trained operators Wear dust masks and goggles Ensure that site is clean and existing straw bales are properly stacked to minimize the risk of the bales falling |
| Moving straw from truck to bunker | Slipping tripping and falling Collision with equipment or workers Dust exposure Impact from falling bales | Low | Wear steel toed boots with adequate grip Beware of equipment and workers Workers to wear hi viz vests Trained operators Equipment inspections completed Wear dust masks, goggles Ensure that the bottom bales are not stacked too tightly against the existing stack to allow the bales on top of it to be stored safely. Do not stack the bales more than five layers high. Do not walk or stand right beside stacks of bales |
| Cleaning truck bed of straw debris | Slipping tripping Truck roll away Dust exposure Falling Strain/sprain | Moderate | Wear steel toed boots with adequate grip Ensure truck is turned off and has brakes set Wear dust masks and goggles Ensure 3 point contact when going up and down from truck bed Ensure using proper tool for the job and not overreaching |
| Other Recommendations: Utilize frequent tailgate meetings to ensure all workers/contractors are aware of hazards. |

# Text boxes

Disclaimer: This resource is intended for guidance and employers are advised to customize this document or design their own to meet their business needs and legal obligations. Once customized from its original content this disclaimer may be removed to function as part of your Safety Program. This resource does not relieve persons using it from their responsibilities under applicable legislation. If you need assistance contact us at www.AgSafeBC.ca